I/O Channel	PTR	AS	PTD	V1	V2	V3	V4	V5	V6	S1	S2	S3	S4	S5	S6	P1	X	Y	Z	A
I/O Identification	Purge and Trap Device Ready on Pos+ Input	Autosampler Start Pos+ Output Pulse 200ms	Purge and Trap Desorb Start Pos+ Pulse 200ms	Valve 1 Syringe/Sample	Valve 2 H2O Rinse	Valve 3 Calibration Standard	Valve 4 Waste	Valve 5 Gas Flush	Valve 6 Needle Gas Flush	Switch 1 If ON Vial Present in X Axis	Switch 2 If ON Needle Carriage in UP Position	Switch 3 If ON Standard Skip Ring Present	Switch 4 If On Sample Syringe in Down Pos	Switch 5 If On Standard Syringe in Down Pos	Switch 6 If ON Lid on Autosampler Closed	Pressure Sensor Rinse H2O	Stepper 1 X Axis Vial Position Advance	Stepper 2 Y Axis Sample Syringe	Stepper 3 Z Axis Needle Carriage	Stepper 4 A Axis Standard Syringe
I/O Channel	PTR	AS	PTD	V1	V2	V3	V4	V5	V6	S1	S2	S3	S4	S5	S6	P1	X	Y	Z	A